## Slide 1: Sandbox Assembly and Startup
For STEM Fair
Nick Carter 101918
Ver. 3

## Slide 2: WIRING
KINECT
Projector
FAN
AC OUTLET STRIP
PC
USB 2.0
POWER
HDMI
screen
USB 3.0
USB HUB
Wart.
HDMI
AC
Power

## Slide 3: Turning up
Projector - ON
  Power Switch is under velcro by power cord. Push button for 5 seconds until light goes from red to green.
  No other settings need be touched
KINECT – ON
  No power switch
  Power from USB power adaptor.
PC – set to never shut off with external power

## Slide 4: MAGIC SAND APP.
Turn on PC – power button at right by screen.
  Press until screen shows starting.
  Wait for pictorial login screen
Login - select user “Sandy Box”
  Password “S@ndbox2017”
  All other users must be signed out (power cycle if in doubt)
App startup
  Double click on screen icon for Magic Sand
  You should get a DOS black window with white text showing script execution.
  It should find projector and Kinect or it will indicate “not found”
  It will then bring up Sandbox GUI.
  You should see the sandbox image in the window.
  You should see an image projected on the sand (Windows wallpaper)

## Slide 5: In the Sandbox GUI
Starting the App – saved calibration
  Check if it indicates calibrated on lower left
    If YES
    Use prior saved calibration file just click “RUN” in top right.
  Otherwise see Calibration page
Changing animal numbers
  Lower right are sliders and numbers to set these.
Removing all animals
  There is a radio button lower right

## Slide 6: Games
Switching Games
  “f” - Animal Game – 2 players trapping bunnies and fish on your side – timed session for best score.
  “space” - Island Game – difficult and not recommended as has long timeouts and vague instruction.
  “m” - Mother Game – guide fish and bunnies to their moms by changing terrain. Hitting “m” again resets mothers to random locations.
  Or use push-buttons on box if equipped

## Slide 7: Shutdown
Projector
  Press power button until fan stops. It may take a while as the projector needs to cool a bit first.
Kinect.
  Nothing special. Can be unplugged any way.
PC
  Close Sandbox app
  Normal Windows shutdown.
Top FAN – turn off

## Slide 8: Troubleshooting 1
The Projector will shut off if it gets too hot. If it does, the Sandbox program may hang up requiring a PC reboot. Repeat start up sequence.
The Kinect may lose connection to PC. This will be audible if PC loses device (ping). The USB port on the PC is a bit loose. Make sure it is firmly inserted. Only the USB 2.0 port will work.
  Close Sandbox App if you can. Otherwise reboot.
    If totally stuck hold power button.
    Power it back on and login again.
  Unplug USB hub from PC
  Unplug KINECT from USB hub
  Replug USB Hub into PC (ping)
  Replug Kinect into HUB (ping).
  Restart Sandbox program.

## Slide 9: Troubleshooting 2
LOW Frame rate - The response is sluggish
  Close app and reboot PC and restart everything
  This will log out any other user.
Alignment
  In the initial view of the Application, the sandbox should be central and the rectangle edges aligned horizontally and vertically with the window.
  This makes the Manual drawing of sand region better.
  If not aligned, adjust Kinect and projector positions to make it aligned. If you are not using the iron frame the sandbox too can be moved to make the alignment.

## Slide 10: Calibration – via GUI
This works best in very dim lighting. Turn off lights or use black sheet to reduce lighting over sandbox.
If you do not see a picture of the sandbox but just white:
  Click on – Advanced – click radio button for the image not the sand height
Click on - Calibration|Manually Draw Sand Region
  Use the mouse to draw a rectangle around the sand edges.
Click on - Automatically Calibrate Kinect & Projector
  Prompt will ask for sand to be flattened – do this and click OK
  5x5 checkerboards will be projected at various locations on the sand. There is a count of successful steps (total 5) at GUI lower left.
  Prompt will ask for cover over sandbox – put wood cover on and click OK – this is most critical for low light need.
  5x5 checkerboards will be projected at various locations on the sand. There is a count of successful steps (total 5) at GUI lower left.
  Some delay for calculation ensues after step 5 completes.
  The GUI will display calibration successful at lower left when done
  Topographical colors should be projected
  Remove cover and you can play in the sand.

## Slide 11: Changes
Ver 2 - 050218
  Calibration - change on Advanced menu reference
Ver 3 – 030219
  Changed user names